## Slide 1
CMP6207 · MODERN DATA STORES
A document store for household automations
MongoDB replica set rs0, MQTT, and a Node.js rule engine
Shekhar Lamichhane

## Slide 2
PROBLEM
The pump is switched on, then left alone
A 1,000 litre roof tank can overflow, run dry, or spin while no water moves.
Each sensor sends a different reading: level, flow, pump state, or inlet presence.
The same home also has a study desk and a living-room air conditioner.
The record that matters after a failure is the incident, not every sensor sample.
CMP6207 · Shekhar Lamichhane
2 / 12

## Slide 3
WHAT WAS BUILT
One API, three databases, one replica set
smart_water keeps the roof tank. It warns at 90% and stops the pump at 98%.
smart_focus turns the desk lamp to 6500 K at full brightness when someone sits down.
smart_climate starts cooling above 28°C and stops at 26°C.
Sensors are simulated. The status page and Telegram talk only to the API.
CMP6207 · Shekhar Lamichhane
3 / 12

## Slide 4
PATH
A reading comes in. A command can go back.
Simulator publishes one MQTT message per device.
The API checks the topic, validates the reading, and stores telemetry at w:1.
device_latest is replaced, then only that subsystem's rules run.
A cutoff or a button press publishes a command at QoS 1.
CMP6207 · Shekhar Lamichhane
4 / 12

## Slide 5
DATA
The reading stays a document
Flexible payload
telemetry.reading changes with device_type. Level, flow, presence, lamp, and temperature do not share one row of nulls.
Latest, not a scan
device_latest holds the current value. The page and the rules read that. History stays in telemetry for the charts.
Derived litres
Litres and minutes to cutoff are calculated on read from the 1,000 L capacity. They are not a separate sensor.
CMP6207 · Shekhar Lamichhane
5 / 12

## Slide 6
RULES
Water rules, in the order that matters
Warning at 90% with the pump on: an incident, no command.
Overflow at 98%: pump off. Dry-run: pump on and no inlet water, so the pump stops.
Pump failure: pump on, water present, almost no flow, level not rising.
Abnormal flow: pump off and water still moving. Low tank at 15%: incident only.
If an off command is ignored for 30 seconds, the open incident becomes a confirmed fault.
CMP6207 · Shekhar Lamichhane
6 / 12

## Slide 7
OTHER ROOMS
Same engine, different conditions
Study desk
Presence true sets the lamp to study mode. Presence false turns it off. The rule does not repeat while the lamp is already in that state.
Living room
Cooling starts only when the room is above 28°C and the unit is off. It stops at 26°C while cooling, so it does not chatter at one threshold.
One open incident
A rule is skipped while an incident for that rule_id is still open. An old fault can hide a new alert until it is closed.
CMP6207 · Shekhar Lamichhane
7 / 12

## Slide 8
REPLICA SET
rs0 already has three members
Ports 27017, 27018, and 27019. One primary, two secondaries. Do not initiate the set again.
The rule engine reads the primary, so it does not act on a stale secondary.
Telemetry uses w:1. Incidents use w:"majority", so a cutoff can survive one node.
The election test is still to record: stop the primary during an overflow and show the incident remains.
CMP6207 · Shekhar Lamichhane
8 / 12

## Slide 9
NOTIFY
Every incident is stored. Telegram is optional.
A notification is written for a rule and for a manual On or Off.
Telegram is used only when the token is the full BotFather value and the chat id is the person's own id.
The API reads .env at startup. Restart it after either value changes.
If Telegram rejects the token, the alert still appears on the Alerts page.
CMP6207 · Shekhar Lamichhane
9 / 12

## Slide 10
SHOW IT
One simulator moves one room
npm run seed, then npm run dev, then open localhost:3000.
overflow, dry-run, pump-failure, abnormal-flow, and fault are tank cases. Run one at a time.
study sits someone at the desk, then leaves. cool warms the room past 28°C.
If only cool is running, the tank and the desk stay on their last stored readings. Stop cool with Ctrl+C.
CMP6207 · Shekhar Lamichhane
10 / 12

## Slide 11
REPORT
About 4,000 words, then the evidence
Appraisal of the document model against a relational schema for these readings.
Cluster write-up for rs0, including the failover run once it is saved.
Rules, three databases, and the demonstration cases already observed.
Screenshots go in evidence/. Do not invent an election time.
CMP6207 · Shekhar Lamichhane
11 / 12

## Slide 12
The tank still stops at 98%.
The desk and the living room use the same path.